## Slide 1: Lecture 5: Interaction of x-rays with matters
Dr. Guohua Cao （曹国华）
caogh@shanghaitech.edu.cn
School of Biomedical Engineering
ShanghaiTech University
3/12/2024

## Slide 2: Lecture 5: Interaction of x-rays with matters
X-ray as EM Radiation
  EM Radiation
  X-rays & Visible Lights
  Energy Quanta of Photon
Atoms and Matters
  Atoms in Human Body
  Atomic Structure
X-ray Matter Interaction
  Photoelectric Absorption
  K-edge Absorption
  Compton Scattering
  Total X-ray Attenuation
  NIST Database
  Relative Contribution of Different Interactions
  Beer’s Law and Attenuation Coefficients (Linear and Mass)
  Dependence of X-ray attenuation on energy, beam hardening
  Signal from X-ray Matter Interaction
  Demo on Signal Processing

## Slide 3: What is x-ray?
Electromagnetic radiation of high energy and very short wavelength (between ultraviolet light and gamma rays) that is able to pass through many materials opaque to light.

## Slide 4: What is x-ray? (count.)
X-ray in medical imaging
20-120 kev
0.01-0.06 nm
1018-1019 Hz
X-ray Therapy 500 keV - Mega-ev
X-ray is EM (electromagnetic) radiations.
Notes: Contrast arises from mainly diff. in photoelectric absorption.
Thus there is high contrast between hard and software tissues

## Slide 5: X-rays vs. visible lights
as lights, share some common properties of all lights
  travel at the speed of light
  wave–particle duality
  common terms: spectrum, monochromatic, polychromatic, coherence, absorption, scattering, attenuation.
yet exhibit its unique properties
  occupies a high-energy region
  of the whole EM spectrum
  highly energetic and
  ionizing radiation with deep
  penetration capability
  Unique terms: photoelectric interaction, Compton scattering, K edge

## Slide 6: Transmission of EM Radiation

## Slide 7: Photon and Energy Quanta
For all EM radiations,
frequency vs. wavelength
energy vs. frequency
 | Frequency | Wavelength | Energy
 | Hz | m | eV
x-ray | 1.00E+19 | 3.00E-11 | 4.14E+04
soft x-ray | 1.00E+18 | 3.00E-10 | 4.14E+03
visible light | 1.00E+15 | 3.00E-07 | 4.14E+00
Terahertz | 1.00E+12 | 3.00E-04 | 4.14E-03
Gigahertz | 1.00E+09 | 3.00E-01 | 4.14E-06
RF - UHF | 3.00E+08 | 9.99E-01 | 1.24E-06
RF - VHF | 3.00E+07 | 9.99E+00 | 1.24E-07
RF - High Freq. | 3.00E+06 | 9.99E+01 | 1.24E-08
RF - Medium Freq. | 3.00E+05 | 9.99E+02 | 1.24E-09
h is Planck constant
h=6.626 x 10-34 J s
1ev = 1.60e-19J
Notes: The FM radio band is from 88 to 108 MHz in ~VHF.

## Slide 8: Atoms in Human Body
https://en.wikipedia.org/wiki/Composition_of_the_human_body
Element | Mass percent | Atomic percent | Electrons per shell | K shell binging energy (keV)
Hydrogen | 10 | 62 | K1 | 0.014
Oxygen | 65 | 24 | K2, L4 | 0.543
Carbon | 18 | 12 | K2, L6 | 0.284
Calcium | 1 | 0.22 | K2, L8, M8, N2 | 4.039

## Slide 9: Structure of Atom
K
L
M
N
Fe: K2,L8,M14,N2

## Slide 10: Photoelectric Absorption
Inner K shell electron gets knocked out to infinity by incident x-rays
Outer L shell electron migrates to the K shell vacancy.
A characteristic x-ray photon is emitted in the process.
In the process, total energy of the incident x-ray photon, ejected electron, and characteristic x-ray photon is absorbed.
The end is a bunch of ionized atoms and free electrons.

## Slide 11: Photoelectric Absorption
In diagnostic x-ray energy range,
absorption  Z3/E3
Energy dependence
   Photoelectric absorption is dominant when x-ray energy is low.
Matter dependence
   Lead (Z=82) is an excellent x-ray absorber and used for shielding x-rays.

## Slide 12: K-edge Absorption
Sudden increase of x-ray attenuation coefficient when incident x-ray photon energy is just above the K shell binding energy of the target atoms.
For K-edge absorption to occur, incident x-ray photons must have energy greater than the k-edge energy of the target atom.
Notes: Introduce K edge imaging

## Slide 13: Compton Scattering
An incoming photon with wavelength  collides with an loosely bounded outer shell electron that is treated as being at rest.
The incoming photon transfers part of its energy to the electron, causing the electron to eject.
The scattered photon has less energy than the incoming photon, or has longer wavelength ’ (> ), to conserve energy.
The scattered photon exits at a certain angle  to the forward direction, to conserve momentum.

## Slide 14: Compton Scattering
Scattering probability is not same at every angle.
Energy of Compton scattered photons
511keV is the energy equal to the rest mass of the electron.
Klein–Nishina distribution of scattering-angle cross sections over a range of commonly encountered energies.

## Slide 15: Total x-ray attenuation
In optics:
  Total attenuation = absorption + scattering
Equivalently, in x-ray imaging:
  Total x-ray attenuation = photoelectric absorption + scattering

## Slide 16: Relative contributions
Figure shows the relative contributions of photoelectric absorption and Compton scattering to the total attenuation coefficient of water.
Photoelectric absorption dominates at the low energy while Compton scattering dominates at high energy.
Photoelectric absorption dominates
Compton scattering dominates

## Slide 17: NIST Database
https://physics.nist.gov/PhysRefData/Xcom/html/xcom1.html

## Slide 18: NIST: X-ray reference
https://physics.nist.gov/PhysRefData/Xcom/html/xcom1.html

## Slide 19: Beer’s law & X-ray linear attenuation coefficient
Beer-Lambert law

## Slide 20: Mass Attenuation Coefficient
μ/ρ = mass attenuation coefficient (cm2/g)
  μ = linear attenuation coefficient (cm-1)
  ρ = density (g/cm3)
ρx = mass thickness (g/cm2)
  x = path length (cm)

## Slide 21: X-ray attenuation of various tissues
Energy dependence of the linear attenuation coefficient:
linear attenuation coefficient is higher at lower x-ray energy, and lower at higher x-ray energy.
Notes: Note Bone vs fat & muscle; muscle vs fat in x-ray contrast.

## Slide 22: X-ray Beam Hardening
A
C
B
original
Energy dependence of the linear attenuation coefficient: linear attenuation coefficient is higher at lower x-ray energy and lower at higher x-ray energy.

## Slide 23: Beam Hardening
Average energy becomes higher, that is, hardened.

## Slide 24: Signal from X-ray Matter Interaction
X-ray Detector
X-ray Source
1
2
I0
3
N
…
I
Object
Notes: Before we move onto explaining how CT works, let’s first take a look at the conventional 2D radiography.
In conventional 2D radiography, such as chest x-ray imaging, a patient stands between an x-ray source and an detector. During image acquisition, nothing rotates. After a short x-ray exposure, the transmitted x-ray intensity after the object is recorded into a 2D radiograph image, in this case a chest x-ray image, is formed. An example chest x-ray image is shown in the right.
(click)
In conventional radiography, the 3D volume of a human body is compressed along the x-ray direction to a 2D image, therefore it does not have the ability to resolve overlapping tissues.

## Slide 25: What signals do we measure?
x
1
2
I0
3
N
…
I
S = logI0/I= xi
 S=Total attenuation in the x-ray path length
I, I0 are the raw data measured by the detector.
S is the signal pre-processed from the raw data I, I0.
Notes: Unlike 2D radiography, CT is a 3D modality. It can resolve the local contrast even within a very thin slice. So, how a CT works?
In CT, an object is also positioned between an x-ray source and detector. And we also measure the transmitted x-ray intensity after the object. The differences are mainly in two parts: (1). In addition to the transmitted x-ray intensity after the object, we also measure the x-ray intensity before the object. (click) With both intensity measurements, we can derive the signals during CT data acquisition following the Beer’s Law. The signal essentially is the integration of attenuation along the x-ray beam path. (2) (Click) The 2nd difference is for CT we need do rotation and sample the signals from many view angles. The reason for this is closely related to how we reconstruct CT images. Let’s use this simple 4-voxel slice as an example. In this slice, there are four voxel of same dimensions but different attenuation coefficients. If we sample this slice with x-ray from left to right, we got two signals (S1 & S2) from two line integrals, and we have 2 equations. But 2 equations are not sufficient for solving the 4 unknown attenuation coefficients. If we sample this slice with x-ray from another direction, top-to-bottom, we will receive 2 more signals (S3 & S4) from another two line integrals, and we have another 2 equations. Now we have a total of 4 equations. With these 4 equations we can find the 4 unknown attenuation coefficients.

## Slide 26: Matlab Demo
imread()
imagesc()
image matrix operations
  Correction for detector offset
  S=log(I0/I)
  Plot line intensity profile
  Crop the image

## Slide 27
X=imread(‘1.tif’);
imagesc(X);
colormap gray
imagesc(X, [100,2000]);
Offset=imread(‘dark.tif’);
X=X-Offset
Y=imread(‘blank.tif’);
/* convert matrices to double float format for matrix division */
X=double(X);
Y=double(Y);
/* signal */
S=log(Y./X);